Kathmandu Engineering College
Kalimati, Kathmandu

Lab Report on
Instrumentation II

Name: Adarsha Acharya	Sumbitted to:
Group: A1	The Department of
Year: III/I	Electronics, Communication
Roll no: 13	and Information Engineering
Interfacing 8255 PPI with 8085 (mode 1)

Objective
* To configure 8255 PPI in mode 1 and observe it’s application.

Theory
PPI 8255 is general purpose programmable I/O interfacing device. It has 24 pins categorized as groups of 8 pins namely Port A, Port B and Port C. Port C can be further grouped as C upper and C lower but also, it can be used as an individual pin.

The functions of these ports are efined with control word in control register.

8255 can function in two different modes
1) Bit Set/Reset mode (BSR mode)
2) I/O mode

Mode 1 (basic I/O)
In mode1, handshake signals are exchanged between the MPU and peripherals prior to data transfer. Two ports A and B, function as 8-bit I/O ports. They can be configured either as input or output.
When port A is programmed as an input port PC3, PC4 and PC5 are used for control, PC6 and PC7 are used for input or output, as programmed by bit D3 of the control word.
When port A is programmed as an output port PC3, PC6, PC7 are used for control and PC4 and PC3 can be input or output, as programmed by bit D3 of the control word.
When portB is to be programmed as input or output port PC0, PC1 and PC2 are all used for control.

MODE 1 Input control signals
- STB
- IBF
- INTR
- INTE
Mode 1 Output Control Signals
- OBF
- ACK
- INTR
- INTE

Q1) Configure 8255A as Port A in mode 1 as input, and Port B in mode 0 as output. Read the port A and Display the content in port B.
(Use maskable interrupt M6.5)
Solution:
Control word for configuring 8255A for given condition is given below:
D7	D6	D5	D4	D3	D2	D1	D0
0	0	1	1	0	0	0	0

=BOH
Since we have to read data from port A, so setting the STB from port A we have to set PC4, then IO BSR mode. Control word is given below:

D7	D6	D5	D4	D3	D2	D1	D0
0	0	0	0	1	0	0	1

=09H

For using maskable interrupt the control word is given by,

D7	D6	D5	D4	D3	D2	D1	D0
0	0	0	0	1	1	0	1

=0DH

Mnemonics	Op Code	Address
MVI A, BOH / OUT 83H / MVI A, 09H / OUT 83H / EI / MVI A 0DH / SIM / JMP 800CH / IN 80H / OUT 81H / JMP 8F39H	3EH / B0H / D3H / 83H / 3EH / 09H / D3H / 83H / FBH / 3EH / 0DH / 30H / C3H / 0CH / 80H / D3H / 80H / D3H / 81H / C3H / 39H / 8FH	8000H / 8001H / 8002H / 8003H / 8004H / 8005H / 8006H / 8007H / 8008H / 8009H / 800AH / 800BH / 800CH / 800DH / 800EH / 800FH / 8010H / 8011H / 8012H / 8013H

Q2) Configure 8255A as Port A in mode 0 as output, and Port B in mode 1 as input. Read the port B and Display the content in port A.
(Use maskable interrupt M6.5)
Solution:
Control word for configuring 8255A for given condition is given below:
D7	D6	D5	D4	D3	D2	D1	D0
0	0	0	0	0	1	1	0

=86H
Since we have to read data from port B, so setting the STB from port B we have to set PC2, then IN BSR mode. Control word is given below:

D7	D6	D5	D4	D3	D2	D1	D0
0	0	0	0	0	1	0	1

=09H

For using maskable interrupt the control word is given by,

D7	D6	D5	D4	D3	D2	D1	D0
0	0	0	0	1	1	0	1

=0DH

Mnemonics	Op Code	Address
MVI A, 86H / OUT 83H / MVI A, 05H / OUT 83H / EI / MVI A 0EH / SIM / JMP 800CH / IN 81H / OUT 80H / JMP 8FB3H	3EH / 86H / D3H / 83H / 3EH / 05H / D3H / 83H / FBH / 3EH / 0EH / 30H / C3H / 0CH / 80H / D3H / 81H / D3H / 80H / C3H / B3H / 8FH	8000H / 8001H / 8002H / 8003H / 8004H / 8005H / 8006H / 8007H / 8008H / 8009H / 800AH / 800BH / 800CH / 800DH / 800EH / 800FH / 8010H / 8011H / 8012H / 8013H / 8014H / 8015H

Discussion:
Using Port A and Port B as input and output one by one, we checked the functionality of the interrupt signals and their respective addresses where their respective code runs from.

Conclusion
Hence, we learnt how 8255PPI works in mode 1 and how ports produce and accepts handshaking signals.