Kathmandu Engineering College
Kalimati, Kathmandu

Lab Report on
Instrumentation II

Name: Adarsha Acharya	Sumbitted to:
Group: A1	The Department of
Year: III/I	Electronics, Communication
Roll no: 13	and Information Engineering
Introducing 8255 PPI with 8085 (mode 0)

Objective
* To configure 8255 PPI in mode 0 and observe it’s application.

Theory
PPI 8255 is general purpose programmable I/O interfacing device. It has 24 pins categorized as groups of 8 pins namely Port A, Port B and Port C. Port C can be further grouped as C upper and C lower but also, it can be used as an individual pin.

The functions of these ports are efined with control word in control register.

8255 can function in two different modes
1) Bit Set/Reset mode (BSR mode)
2) I/O mode

Mode 0 (basic I/O)
There is a simple I/O configuration for all ports (A, B, C) There is no handshaking in this mode. The outputs are latched but inputs are not. It consists of two 8 bit-ports, A and B and two 4 bit Ports, C-upper and C-lower. Any of these ports can be configured as input or output.

Q1) Configure 8255A as Port A in mode 0 as output, and Port B in mode 0 as input.

Mnemonics	Op Code	Address
MVI A, 82H / OUT 83H / IN 81H / OUT 80H / RST 5	3EH / 82H / D3H / 83H / DBH / 81H / D3H / 80H / EFH	8000H / 8001H / 8002H / 8003H / 8004H / 8005H / 8006H / 8007H / 8008H

Output
Port A : 01110111
Port B: 01110111

Discussion:
Port “A” was configured in mode 0 as an output port and port “B” as in the input port, also in mode 0. To do this, control word 82H was stored in control Register. The input provided in Port “B” was observed as output in Port “A”.

Q2) Configure 8255A as Port A mode 0, output, and Port B as mode 0 and output as well.

Mnemonics	Op Code	Address
MVI A, 80H / OUT 83H / MVI A, 07H / OUT 81H / OUT 80H / RST 5	3EH / 80H / D3H / 83H / 3EH / D7H / D3H / 82H / D3H / 80H / EFH	8000H / 8001H / 8002H / 8003H / 8004H / 8005H / 8006H / 8007H / 8008H / 8009H / 800AH

Output:
Port A: 11010111
Port B: 11010111

Discussion: In this D7H was providing by both part A and port B as output D7H in binary is 11010111 and from LED’s we observed the MSB and LSB of Port A and Port B.

Q3) Configure 8255 PPI as Port A (mode0, input) and Port B (mode 1, output)

Mnemonics	Op Code	Address
MVI A, 90H / OUT 83H / IN 80H / OUT 81H / STA 8FF1H / CALL 044CH / HLT	3EH / 90H / D3H / 83H / DBH / 80H / D3H / 81H / 32H / F1H / 81H / CDH / 4CH / 04H / 76H	8000H / 8001H / 8002H / 8003H / 8004H / 8005H / 8006H / 8007H / 8008H / 8009H / 800AH / 800BH / 800CH / 800DH / 800EH

Q4) WAP to send port C pins and Port C pins associated to switched as top of the given 8155 PPI module.

Mnemonics	Op Code	Address	Output
MVI A, 90H / OUT 83H / MVI A, 01H / OUT 83H / RST5	3EH / 90H / D3H / 83H / 3EH / 01H / D3H / 83H / EFH	8000H / 8001H / 8002H / 8003H / 8004H / 8005H / 8006H / 8007H / 8008H	PC0, 01H, LED1 on / PC1, 03H, LED2 on / PC2, 05H, no LED on / PC3, 07H, LED3 on / PC4, 09H, no LED on / PC5, 0BH, LED4 on / PC6, 0DH, no LED on / PC7, 0FH, LED5 on

Discussion:
Depending upon the input provided at 8055H address for PC0, PC1, PC7 we could observe the port C pins associated to switched in PPI

Conclusion
Hence 8255A PPI was interfaced with 8085 microprocessor in Mode 0 for input and output.